## Slide 1: Design Patterns for Large Scale Data Movement
Hans Jespersen
VP Systems Engineering
hans.jespersen@solacesystems.com

## Slide 2: Data Movement Patterns
The right solution depends on the problem you’re solving
  Update rates?
  Fan-in or fan-out?
  Payload size?
  Guarantee required?
http://www.dreamstime.com/stock-images-wispy-blue-spirals-pattern-image1983204
  Real-time or intermittent?
  Any weird networks?
  Acceptable latency?
  Humans or machines?

## Slide 3: Latency Required
Some not sensitive at all
  Batch updates
Seconds often good enough
  Database sync
  User interfaces
Others measure in milli- or micro-seconds
  Algo trading
  Industrial controls
Chart: 
| Network Distance | Number of Messages | Distribution Frequency | Message Size | Importance of Guarantee | Latency Sensitivity
Max | 10 | 10 | 10 | 10 | 10 | 10
Required Latency
Not Critical
Low as Possible

## Slide 4: Network Distance
Co-location for max speed
  Minimize speed of light
LAN for many apps
  10GigE networks
Long distance WAN
  Expensive, limited pipes
  Creates mismatches with other networks
Chart: 
| Network Distance | Number of Messages | Distribution Frequency | Message Size | Importance of Guarantee | Latency Sensitivity
Max | 10 | 10 | 10 | 10 | 10 | 10
Network Distance
Co-location
Global WAN

## Slide 5: Number of Messages
Few
  Batch updates
  Simple applications
Moderate
  Risk management
  Order routing
Insane
  Market data
  Click stream analysis
Chart: 
| Network Distance | Number of Messages | Distribution Frequency | Message Size | Importance of Guarantee | Latency Sensitivity
Max | 10 | 10 | 10 | 10 | 10 | 10
Number of Messages
OMG
Whatever

## Slide 6: Degree of Distribution
Point-to-point
Fan-out (many subs)
Fan-in (many pubs)
Mesh
  Synching data between many endpoints
Chart: 
| Network Distance | Number of Messages | Distribution Frequency | Message Size | Importance of Guarantee | Latency Sensitivity
Max | 10 | 10 | 10 | 10 | 10 | 10
Degree of Distribution
Millions of Endpoints
1:1

## Slide 7: Message Size
Small
  Status updates, activity logging events
Medium
  Orders, product BOMs
Large
  Batch updates, media files, product catalogs
Very different stresses on system based on message size and frequency.
Chart: 
| Network Distance | Number of Messages | Distribution Frequency | Message Size | Importance of Guarantee | Latency Sensitivity
Max | 10 | 10 | 10 | 10 | 10 | 10
Size of Messages
Huge
Small

## Slide 8: Importance of Delivery Guarantee
“Best effort” fine for some scenarios
Others require “once and only once”
Sequence matters for some
Some demand failsafe even in DR scenarios
Chart: 
| Network Distance | Number of Messages | Distribution Frequency | Message Size | Importance of Guarantee | Latency Sensitivity
Max | 10 | 10 | 10 | 10 | 10 | 10
Delivery Guarantee Importance
Very
Not

## Slide 9: Other Considerations
Message
  Format
  Protocol
  Structured/Unstructured
Network
  Availability
  RTT
  Bandwidth cost
Robustness
  Archival
  Caching
  Acceptable MTBF
  HA switchover times
  DR requirements

## Slide 10: Combination of Factors Yields Design Patterns
Some attributes tend to correlate
  # of messages and degree of distribution
Others usually contradict
  Network distance and latency
  Guarantee and latency
Tradeoffs and creative solutions
Chart: 
| Network Distance | Number of Messages | Distribution Frequency | Message Size | Importance of Guarantee | Latency Sensitivity
Max | 10 | 10 | 10 | 10 | 10 | 10
Series 1 | 9 | 5 | 3 | 6 | 2 | 7
Series 2 | 1 | 3 | 5 | 7 | 3 | 1
Number of Messages
Network Distance
Required Latency
Delivery Guarantee Importance
Degree of Distribution
Size of Messages

## Slide 11: Identifying Patterns in Real-World Use Cases
http://www.dreamstime.com/stock-images-wispy-blue-spirals-pattern-image1983204
Examples in this section:
  Trade Order Flow
  Manufacturing Data Sync
  Oil and Gas Monitoring
  Real Time Sports Betting
Use cases unique, but patterns emerge
Notes: 4 patterns (for now)

## Slide 12: Order Flow
Latency matters, but not every microsecond
Usually localized
Continuous, high-rate message flow
Mid-sized messages (1-2Kb)
Messages absolutely must be guaranteed
Chart: 
| Network Distance | Number of Messages | Distribution Frequency | Message Size | Importance of Guarantee | Latency Sensitivity
Max | 10 | 10 | 10 | 10 | 10 | 10
Series 1 | 2 | 9 | 5 | 3 | 10 | 8



Number of Messages
Network Distance
Required Latency
Delivery Guarantee Importance
Degree of Distribution
Size of Messages

## Slide 13: Order Flow; Architecture
Smart Order Router
Back Office
Applications
Management & Monitoring
Client Gateways
Exchange Gateways
Disaster
Recovery Site
Exchanges
Clients
Slow Subscribers
Message Bus
Real Time Sync

## Slide 14: Order Flow; Similar Use Cases
Credit card processing
  Long-distance WANs
  latency in hundreds of milliseconds
Need a way to correlate which use case is which color on the chart.
Number of Messages
Network Distance
Required Latency
Delivery Guarantee Importance
Degree of Distribution
Size of Messages
Chart: 
| Network Distance | Number of Messages | Distribution Frequency | Message Size | Importance of Guarantee | Latency Sensitivity
Max | 10 | 10 | 10 | 10 | 10 | 10
Series 1 | 2 | 9 | 5 | 3 | 10 | 8
CC Processing | 4 | 8.8 | 4 | 5 | 10 | 3
Inventory | 2 | 9.5 | 9 | 6 | 10 | 5
Financials | 4 | 7 | 3.8 | 4.1 | 10 | 2.8
E-commerce
  Higher volumes
  Higher guarantee required
Logistics scheduling
  Less latency sensitive
  More likely to include WANs

## Slide 15: Manufacturing Data Sync
Geographically distributed
100% delivery guarantee required
Data rate is use case specific – will assume lots of medium (< 5K) messages.
Number of endpoints use case specific, assume 10 manufacturing locations
Build from the background image on prior slide
Chart: 
| Network Distance | Number of Messages | Degree of Distribution | Message Size | Importance of Guarantee | Required Latency
Max | 10 | 10 | 10 | 10 | 10 | 10
M2M | 10 | 5 | 5 | 3 | 10 | 1



Number of Messages
Network Distance
Required Latency
Delivery Guarantee Importance
Degree of Distribution
Size of Messages

## Slide 16: Manufacturing Data Sync; Architecture
Applications &
Databases
Maximizing
Bandwidth
Fanout
at Edge
Smart
Buffering

## Slide 17: Manufacturing Data Sync; Similar Use Cases
Real Time Risk Management
  Smaller messages
  Latency more important
Number of Messages
Network Distance
Required Latency
Delivery Guarantee Importance
Degree of Distribution
Size of Messages
Chart: 
| Network Distance | Number of Messages | Distribution Frequency | Message Size | Importance of Guarantee | Latency Sensitivity
Max | 10 | 10 | 10 | 10 | 10 | 10
Manfacturing | 10 | 5 | 5 | 3 | 10 | 1
Risk Mgmt | 8 | 7.5 | 4 | 2.2 | 10 | 3.5
Inventory | 8 | 6 | 7 | 6.5 | 9.5 | 1.2
Financials | 8.5 | 7 | 2.8 | 5.3 | 10 | 2
Retail Global Inventory
  Messages can be larger
  Distribution can be more
Real Time Financials
  Messages larger
  Distribution less (collecting to 1 location)

## Slide 18: Oil & Gas Pipeline Monitoring
Wifi, Satellite, proprietary and other unreliable networks
Degree of distribution off the charts. In this case, fan-in.
Messages usually pretty small, unless batch
Latency unimportant
Level of guarantee use case specific, assume status messages (ie. guarantee not essential)
Chart: 
| Network Distance | Number of Messages | Degree of Distribution | Message Size | Importance of Guarantee | Required Latency
Max | 10 | 10 | 10 | 10 | 10 | 10
M2M | 10 | 10 | 10 | 2 | 6 | 2



Number of Messages
Network Distance
Required Latency
Delivery Guarantee Importance
Degree of Distribution
Size of Messages

## Slide 19: Oil & Gas Pipeline Monitoring; Architecture
Pipeline Sensors
Collection
Caches
Wireless
Analytics
Engines
Big Data & Databases
Unreliable Networks
Big Data Loading
Message Bus
Real Time vs. Delayed Analytics

## Slide 20: Oil & Gas Pipeline Monitoring; Similar Use Cases
Smart Grid
  Small messages
  Massive distribution
Chart: 
| Network Distance | Number of Messages | Distribution Frequency | Message Size | Importance of Guarantee | Latency Sensitivity
Max | 10 | 10 | 10 | 10 | 10 | 10
O&G Pipe | 10 | 10 | 10 | 2 | 6 | 2
Smart Grid | 8 | 9.5 | 10 | 1.6 | 7.1 | 1.5
Transportation | 6.5 | 9.2 | 7.8 | 4.1 | 8.3 | 1
PoS | 9 | 8 | 7 | 5 | 9 | 1
Number of Messages
Network Distance
Required Latency
Delivery Guarantee Importance
Degree of Distribution
Size of Messages
Transportation Monitoring
  Fewer endpoints
  Bigger messages
Retail Point of Sale
  More predictable networks
  Guarantee more important

## Slide 21: Real-Time Sports Betting
Huge message volumes (in this case fan-out)
Low level of guarantee for any one outbound message
High level of guarantee for inbound messages
Tiny messages
Network is the internet + mobile carriers
Latency (beyond network latency) is important
Chart: 
| Network Distance | Number of Messages | Distribution Frequency | Message Size | Importance of Guarantee | Latency Sensitivity
Max | 10 | 10 | 10 | 10 | 10 | 10
Series 1 | 7 | 8 | 8 | 1 | 3 | 6



Number of Messages
Network Distance
Required Latency
Delivery Guarantee Importance
Degree of Distribution
Size of Messages

## Slide 22: Real-Time Sports Betting; Architecture
Highlight the degree of fan out, connection counts, event logging, real time analysis for odds adjustment
Mobile Customers
Web
Customers
Streaming
Odds Data
Clickstream
& Marketing
Security & Fraud Detection
Customer & Betting Apps
Odds & Analytics
Data Streaming
Huge Connection Counts
Low Latency
Big
Data
Message Bus

## Slide 23: Real-Time Sports Betting; Similar Use Cases
Mobile Social Updates
  Latency less important
  Distribution far greater
Chart: 
| Network Distance | Number of Messages | Distribution Frequency | Message Size | Importance of Guarantee | Latency Sensitivity
Max | 10 | 10 | 10 | 10 | 10 | 10
Sports betting | 7 | 8 | 8 | 1.5 | 3 | 6
Mobile Social | 8 | 10 | 9.5 | 2 | 3.5 | 2.5
Travel | 6.5 | 5 | 5 | 2.5 | 5 | 8
MDD | 9 | 9.5 | 10 | 1.1 | 1 | 7.8
Number of Messages
Network Distance
Required Latency
Delivery Guarantee Importance
Degree of Distribution
Size of Messages
Real Time Travel Alerting
  Each message more important
  Volumes much lower
Market Data Distribution
  Latency even more important
  Volumes often much higher
  Loss often tolerable

## Slide 24
Chart: 
| Network Distance | Number of Messages | Distribution Frequency | Message Size | Importance of Guarantee | Latency Sensitivity
Max | 10 | 10 | 10 | 10 | 10 | 10
Sports betting | 7 | 8 | 8 | 1.5 | 3 | 6
Mobile Social | 8 | 10 | 9.5 | 2 | 3.5 | 2.5
Travel | 6.5 | 5 | 5 | 2.5 | 5 | 8
MDD | 9 | 9.5 | 10 | 1.1 | 1 | 7.8
Order Flow | 2 | 9 | 5 | 3 | 10 | 8
CC Processing | 4 | 8.8 | 4 | 5 | 10 | 3
Inventory | 2 | 9.5 | 9 | 6 | 10 | 5
Financials | 4 | 7 | 3.8 | 4.1 | 10 | 2.8
Manfacturing | 10 | 5 | 5 | 3 | 10 | 1
Risk Mgmt | 8 | 7.5 | 4 | 2.2 | 10 | 3.5
Inventory | 8 | 6 | 7 | 6.5 | 9.5 | 1.2
Number of Messages
Network Distance
Required Latency
Delivery Guarantee Importance
Degree of
Distribution
Size of Messages

## Slide 25: Summary
Questions?